Errata Supplement to the

Biological and Water Quality Study of the East and West Branches of the DuPage River and the Salt Creek Watersheds

Cook, DuPage, Kane and Will Counties, Illinois

Midwest Biodiversity Institute

Center for Applied Bioassessment and Biocriteria

P.O. Box 21561

Columbus, OH 43221-0561

Submitted to:

The Conservation Foundation

10 S. 404 Knoch Knolls Road
Naperville, IL 60565

Technical Report MBI/2008-12-3

## Purpose of Errata

Subsequent to the publication of the Biological and Water Quality Study of the East and West Branches of the DuPage River and the Salt Creek Watersheds in 2008, the Illinois Environmental Protection Agency (IEPA) drafted revised scoring criteria for the Macroinvertebrate Index of Biotic Integrity (MIBI).  Tables and graphs appearing in the original document based on MIBI scores have been reproduced here with scores adjusted based on the new, draft scoring criteria.  Where practical, adjusted scores have been either superimposed over old scores, or graphs have been drawn side-by-side to show the scope of differences.  Tables, however, have been reproduced with adjusted scores, and annotated for the few cases where the scoring adjustment resulted in a change in condition status for the waterbody.  Similarly, IEPA released a draft, revised manual for scoring fish IBIs; however, unlike the systemic changes to the MIBI, the only correction needed to the fish IBI scores was for 22 samples where less than 50 individuals were collected.  The scores for these 22 samples were adjusted according to IEPA recommendations.  The low-end adjustments resulted in no significant difference in scores.

List of Errata

Salt Creek

Table 4	5

Figure 9	8

Figure 11	9

# Figure 55	10

Figure 56	11

Figure 57	12

Figure 58	13

East Branch DuPage River

Table 10	15

Figure 59	16

Figure 99	17

Figure 100	18

West Branch DuPage River

Table 16	20

Figure 101	23

Figure 103	24

Figure 129	25

Figure 130	26

Itemized changes to text	27

Low-end adjustment to fish IBI scores	38

Errata Occurring in the Chapter

Biological and Water Quality - Salt Creek

Errata:  Table 4 is reproduced here with revised MIBI scores, low-end adjusted fish IBI scores, and updated attainment status where revised scores resulted in a change in status.  Low-end adjusted fish IBI scores and sites where attainment status changed are noted with an asterisk.

River 	Site 	Fish 	IEPA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-840	Arlington Heights Branch Salt Creek

4.00	SC06	30.5	10.9	Non	7.7

1.50	SC45	45.0	25.5	Non	10.0

0.25	SC08	57.5	20.2	Non	12.7

95-845	Baldwin Creek

2.00	SC05	64.0	16.1	15.5	Non	2.0

95-850	Salt Creek

39.50	SC04	43.5	20.3	15.0	Non	6.3

36.00	SC07	75.5	19.3	19.5	Non	16.0

32.00	SC15	44.0	40.7	20.0	8.5	Non	32.0

29.00	SC43	47.0	29.7	18.5	7.6	Non	60.0

27.00	SC42	67.5	42.1	18.0	6.4	Non	53.5

25.00	SC41	58.5	46.5	12.0*	4.3	Non	70.0

24.50	SC40	63.5	43.2	13.0*	4.4	Non	75.0

23.50	SC34	54.0	44.6	21.0	8.0	Partial*	76.0

23.00	SC35	46.5	33.5	19.0	7.1	Non	80.0

22.50	SC23	71.0	41.1	21.5	7.2	Partial*	84.0

20.50	SC39	74.0	39.4	23.0	6.6	Partial*	79.0

18.00	SC38	84.0	39.2	16.0	5.4	Non	87.0

17.50	SC37	76.5	39.0	15.5	5.1	Non	95.0

17.00	SC51	74.5	37.3	12.5	4.7	Non	95.0

16.50	SC57	71.5	41.1	14.0	5.4	Non	95.0

13.50	SC55	47.5	21.9	17.5	5.4	Non	102.0

12.50	SC56	40.5	17.9	18.5	6.0	Non	107.0

11.00	SC53	39.5	17.4	19.0	6.9	Non	110.0

10.50	SC52	82.5	43.1	28.0	8.9	Partial*	112.0

8.00	SC49	87.5	44.9	23.5	4.6	Partial*	114.0

3.00	SC54	79.0	55.1	22.0	6.0	Partial*	145.0

0.50	SC29	77.0	17.5	21.5	6.1	Non	150.0

Table 4.  Continued.

River 	Site 	Fish 	CWA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-851	Trib to Salt Creek

2.00	SC01	89.0	18.9	19.0	Non	1.1

95-852	Trib to Salt Creek

0.25	SC02	71.5	25.5	22.5	Partial*	0.9

95-853	Trib to Salt Creek

0.50	SC03	79.5	22.6	17.5	Non	2.5

95-855	Trib to Salt Creek

4.00	SC11	44.5	31.3	18.5	Non	4.0

95-856	Trib to Salt Creek

2.50	SC14	85.0	31.3	18.0	Non	10.0

95-857	Yeargin Creek

0.25	SC12	49.0	14.6	15.0	Non	1.8

95-858	Ginger Creek

1.50	SC30	61.5	27.8	10.0	Non	5.2

95-859	Sugar Creek

0.25	SC33	62.5	16.9	20.0	Non	3.5

95-860	Addison Creek

10.50	SC24	37.5	8.3	10.0*	Non	2.0

8.00	SC26	45.0	15.8	4.0*	Non	5.0

5.00	SC27	62.5	38.3	18.0	Non	10.0

2.50	SC48	52.5	13.5	15.5	Non	18.0

1.50	SC28	55.5	12.8	20.5	Non	20.0

95-861	Trib to Addison Creek

0.50	SC25	51.5	9.0*	Non	1.0

95-870	Spring Brook

6.50	SC21	56.5	10.0	13.0*	Non	2.0

6.00	SC46	71.5	21.4	11.0	Non	3.5

4.50	SC18	38.0	38.5	12.0	Non	5.1

2.50	SC47	60.0	19.4	22.0	Non	10.0

0.25	SC16	44.5	19.0	22.0	Non	14.2

Table 4.  Continued.

River 	Site 	Fish 	CWA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-875	Oakbrook Creek

0.50	SC36	64.5	16.0*	Non	0.8

0.25	SC32	67.5	16.5	24.5	Non	1.2

95-881	Trib to Meacham Creek

0.25	SC20	85.5	16.7	11.5	Non	2.0

95-882	Westwood Creek

0.50	SC22	61.0	12.8	18.0	Non	4.0

Figure 9.  Distributions of macroinvertebrate and fish Index of Biotic Integrity (IBI) scores for sites sampled in 2007 from the Salt Creek basin.  Results are stratified by drainage area.  The dashed line in each plot shows the minimum score needed for the indicator to meet basic biological quality standards.

Figure 9 - Errata.  Distributions of macroinvertebrate and fish Index of Biotic Integrity (IBI) scores for sites sampled in 2007 from the Salt Creek basin.  Results are stratified by drainage area.  The lower dashed line in each plot shows the minimum score needed for the indicator to meet the basic biological quality standard; the upper dashed line represents the respective 25th percentile score for reference sites.

Figure 11 - Errata.  Locations of sites sampled in the Salt Creek drainage referenced in Table 4.  For specific location information of each site, see Table 5.  Sites now considered in partial attainment of the aquatic life use goal as a result of the scoring adjustment to the macroinvertebrate biotic index are shaded green.   Locations of dams and their names (inset key) referenced in the text are noted on the figure as triangles.  [Errata – the site noted as SC 17 on Meacham Creek in the original figure was not sampled in 2006/07, and has been omitted from this figure.]

Figure 55 - Errata.  Macroinvertebrate IBI (MIBI) scores for the Salt Creek mainstem, 2007, plotted by river mile (from the confluence with the Des Plaines River) in relation to municipal wastewater discharges and locations of combined sewer overflows (CSO).  Dam locations are arrayed along the x-axis as diamond-tipped bars.  Narrative quality ranges are noted on the plot.  MIBI scores adjusted to updated scoring criteria are plotted as filled points.  The dashed horizontal line represents the 25th percentile MIBI score for reference sites.

Figure 56. MIBI and QHEI scores for the Salt Creek mainstem plotted by river mile (left panel), and MIBI scores plotted as a function of QHEI scores (right panel).  The arrow points to the same data point in both plots.  The two MIBI scores in the right panel falling well below the fitted (LOWESS) line are shown as filled circles in both panels.

Figure 56 - Errata. MIBI revised from adjusted scoring criteria and QHEI scores for the Salt Creek mainstem plotted by river mile (left panel), and revised MIBI scores plotted as a function of QHEI scores (right panel).  The arrow points to the same data point in both plots.  The two MIBI scores in the right panel falling well below the fitted (LOWESS) line are shown as filled circles in both panels.

Figure 57.  MIBI scores as a function of QHEI score for the Salt, East Branch and West Branch mainstems (left panel), and mainstem tributaries (right panel).  Fitted lines are from LOWESS smoothing.  The dashed horizontal line shows the boundary between restricted (poor) and limited (fair) narrative ranges. Filled circles indicate sites located in forest preserves, or having comparatively wide riparian buffers.

Figure 57 -Errata.  Revised MIBI scores as a function of QHEI score for the Salt, East Branch and West Branch mainstems (left panel), and mainstem tributaries (right panel).  Fitted lines are from LOWESS smoothing.  The dashed horizontal line shows the boundary between restricted (poor) and limited (fair) narrative ranges. Filled circles indicate sites located in forest preserves, or having comparatively wide riparian buffers.  [Errata – one of the shaded sites in the original tributary plot was actually a Salt Creek mainstem site, and now appears in corrected mainstem plot.]

Figure 58 - Errata.  Revised MIBI scores for sites sampled in the Salt Creek catchment, 2007, plotted by narrative ranges.  The locations of POTWs and dams are noted.

Errata Occurring in the Chapter

Biological and Water Quality – East Branch DuPage River

Errata:  Table 10 is reproduced here with revised MIBI scores, low-end adjusted fish IBI scores, and updated attainment status where revised scores resulted in a change in status.  Low-end adjusted fish IBI scores, and sites where attainment status changed are noted with an asterisk.

River 	Site 	Fish 	CWA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-951	Army Trail Creek

0.25	EB24	54.0	16.1	17.5*	Non	0.3

95-952	Armitage Ditch (tib to E. Branch DuPage)

0.50	EB22	56.5	13.7	17.5	Non	2.2

95-953	Glencrest Creek

0.50	EB15	79.5	25.9	17.0*	Non	3.0

95-954	Lacey Creek

2.00	EB14	45.5	20.3	15.0*	Non	2.0

0.25	EB13	41.0	21.4	24.0	Non	4.0

95-955	Willoway Brook

1.00	EB11	83.0	28.8	16.0	Non	3.0

95-956	22nd St. trib to E. Branch DuPage River

1.00	EB17	71.0	29.2	14.5*	Non	0.8

95-957	Rott Creek

2.00	EB06	63.0	33.1	18.0	0.0	Non	4.0

95-980	East Branch DuPage River

23.50	EB29	59.5	21.3	10.5	Non	2.0

23.00	EB25	34.0	19.4	19.7	Non	2.0

22.00	EB23	76.5	35.8	20.0	Non	5.0

21.00	EB26	45.5	25.5	17.5	Non	12.0

20.50	EB21	39.0	23.4	18.0	Non	14.2

19.00	EB36	52.0	17.9	17.5	Non	16.0

18.00	EB19	55.5	27.6	23.0	Non	18.0

15.50	EB30	63.0	31.1	24.0	8.0	Non	27.2

13.00	EB12	51.5	39.4	25.0	6.5	Non	50.0

11.00	EB31	51.0	32.3	36.0	8.2	Non	58.0

9.50	EB37	42.0	41.7	32.5	6.9	Non	60.1

8.50	EB32	60.5	45.5	35.0	8.5	Partial*	61.0

Table 10.  Continued.

River 	Site 	Fish 	CWA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-980	East Branch DuPage River

7.00	EB33	76.0	49.7	35.5	8.1	Partial*	64.0

6.00	EB35	59.0	30.0	7.7	(Non)	76.4

5.00	EB34	56.5	40.8	25.5	7.3	Non	78.0

4.00	EB39	50.0	12.6	28.0	7.2	Non	78.0

3.00	EB38	82.5	57.3	33.5	8.0	Partial	81.0

95-987	St. Joseph Creek

6.00	EB10	52.0	6.0	14.5*	Non	2.0

4.00	EB08	59.0	10.0	3.0*	Non	4.0

1.00	EB07	67.5	20.0	28.0	Non	10.0

Figure 59. Distributions of macroinvertebrate and fish Index of Biotic Integrity (IBI) scores for sites sampled in 2007 from the East Branch DuPage.  Results are stratified by drainage area.  The dashed line in each plot shows the minimum score needed for the indicator to meet basic biological quality standards.

Figure 59 - Errata.  Distributions of revised macroinvertebrate MIBI scores and fish Index of Biotic Integrity (IBI) scores for sites sampled in 2007 from the East Branch DuPage.  Results are stratified by drainage area.  The dashed line in each plot shows the minimum score needed for the indicator to meet basic biological quality standards.

Figure 99 - Errata.  Original (hollow points) and revised (filled points) macroinvertebrate IBI (MIBI) scores for the East Branch mainstem, 2007, plotted by river mile (from the confluence with the West Branch) in relation to municipal wastewater discharges.  Dam locations are arrayed along the x-axis as diamond-tipped bars with letters corresponding to those in Figure 61.  Narrative quality ranges are noted on the plot.  The dashed horizontal line represents the 25th percentile MIBI score for reference sites.

Figure 100 - Errata.  Revised MIBI scores for sites sampled in the East Branch DuPage River, 2007, plotted by narrative ranges.  The locations of POTWs and dams are noted.

Errata Occurring in the Chapter

Biological and Water Quality – West Branch DuPage River

Errata:  Table 16 is reproduced here with revised MIBI scores, low-end adjusted fish IBI scores, and updated attainment status where revised scores resulted in a change in status.  Low-end adjusted fish IBI scores, and sites where attainment status changed are noted with an asterisk.

River 	Site 	Fish 	CWA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-900	W. Br. DuPage River

34.00	WB30	42.0	26.5	15.0*	Non	2.0

31.90	WB95	58.0	30.4	13.0	Non	5.0

31.60	WB29	58.5	20.5	11.5	Non	5.0

30.10	WB112	64.5	29.1	19.5	Non	5.0

28.70	WB91	60.0	35.1	22.0	Non	9.0

27.40	WB92	63.0	37.5	18.0	Non	9.0

25.60	WB25	54.0	37.7	21.5	Partial*	9.0

21.70	WB128	73.5	47.4	17.0	Non	19.0

21.30	WB115	58.5	19.0	(Non)	19.0

19.20	WB21	82.5	72.4	19.5	Non	19.0

16.00	WB127	68.5	21.0	6.8	(Non)	39.0

13.60	WB16	40.5	46.6	18.5	6.8	Non	40.0

11.70	WB130	62.0	46.7	18.5	6.6	Non	50.0

8.60	WB125	53.5	44.9	17.5	6.5	Non	70.0

8.00	WB131	76.5	38.3	27.0	7.8	Partial*	76.0

6.30	WB126	74.5	65.6	33.5	7.7	Partial	96.0

4.20	WB124	53.6	31.5	7.9	Partial	120.0

0.85	WB12	64.0	65.0	(Full)	150.0

95-902	Trib to W. Br. DuPage River

0.30	WB22	32.5	39.2	14.0	Non	2.0

95-904	Trib to W. Br. DuPage River

1.00	WB27	16.0	35.8	12.0	Non	2.0

95-905	Trib to W. Br. DuPage River

0.15	WB28	32.5	31.8	15.0*	Non	2.0

95-906	Trib to W. Br. DuPage River

2.20	WB93	39.0	20.7	6.5	Non	2.0

1.90	WB94	42.0	27.9	7.0*	Non	2.0

0.90	WB26	32.9	19.0	Non	1.0

Table 16.  Continued.

River 	Site 	Fish 	CWA Goal 	Drain

Mile	ID	QHEI	 MIBI	IBI	MIwb	Attainment	Area

95-910	Kress Creek

5.10	WB05	40.0	32.7	13.5*	Non	5.0

2.70	WB04	44.5	18.0	Non	9.0

0.50	WB06	76.0	37.0	17.5	Non	19.0

95-920	Ferry Creek

2.80	WB08	15.0	15.5*	Non	2.0

0.70	WB10	43.0	21.0	Partial*	0.0

95-925	W. Br. Ferry Creek

0.25	WB09	58.5	32.7	15.0	Non	5.0

95-930	W. Br. Cress Creek

0.20	WB11	66.5	24.0	26.5	Non	2.0

95-940	Bremme Creek

0.25	WB13	45.0	Non	2.0

95-950	Spring Brook

3.30	WB15	43.0	14.3	19.0	Non	2.0

3.00	WB90	67.0	16.5	Non	2.0

0.75	WB14	76.5	19.5	Non	5.0

95-960	Winfield Creek

5.40	WB19	41.0	31.3	16.5	Non	2.0

3.50	WB18	41.0	23.4	15.5	Non	5.0

0.40	WB17	18.0	Non	9.0

95-970	Klein Creek

3.60	WB23	52.5	39.3	21.0	Partial*	5.0

1.00	WB20	67.5	51.3	18.5	Non	9.0

Figure 101. Distributions of macroinvertebrate and fish Index of Biotic Integrity (IBI) scores for sites sampled in 2007 from the Salt Creek basin.  Results are stratified by drainage area.  The dashed line in each plot shows the minimum score needed for the indicator to meet basic biological quality standards.

Figure 101 - Errata.  Distributions of revised macroinvertebrate Index of Biotic Integrity (IBI) and fish Index of Biotic Integrity scores for sites sampled in 2007 from the West Branch of the DuPage River basin.  Results are stratified by drainage area.  The lower dashed, horizontal line in each plot shows the minimum score needed for the indicator to meet basic biological quality standards.  The upper, dashed horizontal lines correspond to respective 25th percentile index scores for reference sites.

Figure 103 - Errata.  Locations and identification of sites sampled in the West Branch DuPage drainage referenced in Table 2.  Sites that partially meet the Illinois EPA aquatic life goal for general use waters are shaded green.  The site WB-12 was in full attainment of the aquatic life goal based a single indicator group (macroinvertebrates).  Sites that are now considered in partial attainment as a result of the scoring adjustment include Ferry Creek (WB-10), Klein Creek (WB-23), and the West Branch mainstem (WB-131).

Figure 129 - Errata.  Macroinvertebrate IBI (MIBI) scores for the West Branch mainstem, 2006, plotted by river mile (from the confluence with the East Branch) in relation to municipal wastewater discharges.  Revised scores are noted as shaded points, while those based on original scoring are hollow.  Dam locations are arrayed along the x-axis as diamond-tipped bars.  Narrative quality ranges are noted on the plot (Restricted = Poor; Limited = Fair; General = Good).  The dashed horizontal line denotes the 25th percentile index score for reference sites.

Figure 130 – Errata.  Revised macroinvertebrate IBI scores plotted by narrative range for the West Branch DuPage River.  Locations of dams and publicly owned treatment works are noted.

Itemized List of Specific Errata to the Text, Table and Figure Captions in the

Biological and Water Quality Study of the East and West Branches of the DuPage

River and the Salt Creek Watersheds

p. 27, 2nd paragraph:   The MAIS method was not used as the multihabitat method was used at all sites.  Hester-Dendy colonizer blockers were set only in the West Branch DuPage River in 2006.  Information from the resulting data was not included in the 2006 report.

p. 40, Table 5.  Macroinvertebrates were collected from Spring Brook RM 6.5 (SC21), but not from Meachem Creek RM 0.35 (SC17) as reported in Table 5.

p. 95, last paragraph, the reference to Meecham Creek was deleted.

p. 150, the box plots draw in Figure 101 are from data from the West Branch of DuPage River, not Salt Creek, as indicated in the original caption.

p. 152, Table 17.  The attainment status for site WB21 should have read non instead of partial because the fish IBI scored in the poor range.

p155, Table 17. The location entry for The West Branch DuPage River at RM 11.70 (WB 130) should read “Downstream Warrenville dam”.

p. 156, Table 17.  The location entry for West Branch Ferry Creek RM 1.5 (WB10) should read “Ferry Creek RM 0.7 (WB10)”.

p. 185, Table 22.  The entry for West Branch Ferry Creek RM 0.7 should read “Ferry Creek RM 0.7”.

Errata Supplement: Low-end Adjusted fish IBI Scores Compared to Original Scores

| SITE ID | Date | River Code | RM | IBI low-end adjusted | Unadjusted IBI |
| --- | --- | --- | --- | --- | --- |
| SC40 | 9/25/2007 | 95-850 | 24.5 | 10 | 13 |
| SC41 | 8/8/2007 | 95-850 | 25.0 | 10 | 7 |
| SC26 | 8/15/2007 | 95-860 | 8.0 | 4 | 3 |
| SC24 | 8/15/2007 | 95-860 | 10.5 | 10 | 10 |
| SC24 | 10/6/2007 | 95-860 | 10.5 | 10 | 10 |
| SC25 | 8/15/2007 | 95-861 | 0.5 | 4 | 3 |
| SC21 | 10/4/2007 | 95-870 | 6.5 | 9 | 6 |
| SC36 | 9/5/2007 | 95-875 | 0.5 | 16 | 26 |
| WB30 | 7/27/2006 | 95-900 | 34.0 | 16 | 17 |
| WB30 | 9/14/2006 | 95-900 | 34.0 | 14 | 10 |
| WB28 | 7/28/2006 | 95-905 | 0.15 | 17 | 14 |
| WB28 | 9/16/2006 | 95-905 | 0.15 | 13 | 15 |
| WB94 | 9/14/2006 | 95-906 | 1.9 | 7 | 5 |
| WB05 | 9/16/2006 | 95-910 | 5.1 | 19 | 14 |
| WB08 | 9/15/2006 | 95-920 | 2.8 | 14 | 16 |
| EB24 | 7/11/2007 | 95-951 | 0.25 | 10 | 7 |
| EB15 | 7/12/2007 | 95-953 | 0.5 | 11 | 11 |
| EB14 | 7/13/2007 | 95-954 | 2.0 | 10 | 7 |
| EB14 | 9/14/2007 | 95-954 | 2.0 | 20 | 16 |
| EB17 | 7/15/2007 | 95-956 | 1.0 | 19 | 13 |
| EB08 | 9/14/2007 | 95-987 | 4.0 | 3 | 2 |
| EB10 | 7/10/2007 | 95-987 | 6.0 | 13 | 11 |

A recent update to the scoring procedures for calculating the Illinois fish Index of Biotic Integrity (IBI) recommended a low-end scoring adjustment for samples containing less than 50 individuals.  The low-end score is based on the summation of metric scores for six taxa richness metrics plus the metric score for percent composition by tolerant species, rescaled to a range of 0-60 (i.e., 60 x the sum of low-end metrics/42).  The following table compares low-end adjusted scores to the original scores at twenty-two sites in the DuPage and Salt Creek study area where less than 50 fish were captured.

Paired sampled t-test Mean Difference =1.045455   95.00% CI = -0.462625 to 2.553534

t = 1.441663 df = 21    P = 0.164145